Installing and Configuring DataFusion Rail Interface

This document describes how to set up the DataFusion rail interface on a Multitrac computer. DataFusion communicates to the rail system through a web service installed on the Multitrac PC. This web service makes the rail drop and pick up points look like Miltrac devices.

Requirements:

- Siemens BoxPC 627B or later with Windows XP. Older PCs with Windows 2000 must be upgraded. The PC must be set up using the latest Siemens setup disk.

- PC Miltrac version 21003 or later. DataFusion only works with expanded protocol Miltrac.

- Mentor version 21800 or later.

Installing:

If the PC was set up using the latest setup disk, the DataFusion web service is already installed. To start and stop the web service, do the following:

- Open up Control Panel

- Double click on “Administrative Tools”

- Double click on “Internet Information Services”

- Expand the tree on the right by clicking on the “+”’s until you see “Default Web Site”

- Click on “Default Web Site” so that it is highlighted.

- On the top tool bar, click on the “Stop” button (the black square) to stop the service. Click on the “Play” button (the black triangle) to start the service.

Make sure the service is started by checking to see if the “Play” button is grayed out.

Configuring:

- Configuring the Web Service

Run the DFConfig program by clicking on “Start”, then run. Enter “C:\Program Files\Milnor\DFConfig\DFConfig.exe” and click OK.

For each drop point and pick up point, do the following:

- Click on “New”

- Enter a name for this bag station

- Enter the Web Service URL for this station. This is the URL on the rail system computer that will handle communications for this station. For an ETech rail system this is typically http://railpro1:3000/tunnelcommunications/x.xml   where x is 1, 2, 3, etc depending on which bag station this is in the ETech controller.

- Enter a Miltrac address for this station.

- If this station will be loading a Milnor device, check “Enable Discharge”. If this station will be receiving from a Milnor device, check “Enable Receive”. If this station will drop more than 1 bag per load, check “Washer-Extractor Loading”.

- Do not change any of the setting under “Advanced” without checking with Engineering.

- Click “Exit” when done

- Configuring Miltrac

- Add a device in Miltrac for each bag station

- Configure each device. Enter X and Y coordinates like you would for any Miltrac device.

- Under Serial Com Port, select “TracInf.DLL”