08MN0***** Monitor Replacement Kit.

The monitor contained in this kit replaces multiple CRT monitors used in the past on Milnor CBW system controllers.  The new monitor auto-syncs to the scan rate of the video signal provided.  This allows one replacement monitor to be used for up to 3 distinct monitor applications in CBW systems.

Mounting the monitor will require adapting the mounting bezel of the new monitor to the existing control box door.  This may require cutting the door opening to fit the new mounting bracket.  Afterward, apply the bezel overlay to conceal the mounting screws and bracket.  This will require drilling holes and mounting the bezel overlay with screws provided.

The new monitor comes with a VGA cable in box.  If you have a VGA or CGA monitor, use the cable in the box.  If you are connecting to a Non-Serial Miltron CBW, you will need an adaptor cable 10YCRTNSP to connect to the edge card connector.  The pictures below show connections which must be completed on a CBW MILTRON (Non Serial Controls) which use an edge card connector on the processor board and a cable connector on the new monitor.

The older monitor used an edge card connector.  The signals must be identified for connection to the new cable connector.  These are shown in the schematic for the CBW and also in the pictures if a schematic is not available.

The splice terminals provided will be used to connect wires of the VGA cable supplied in the box to the edge card wires leaving the processor board of your existing cable.  Cut away the old monitor end of your existing cable and butt-splice the new cable connector to the existing wires.

| Video Signal |  | Edge Connector Pin |  | Cable Connector Pin |  | Butt Splice Wire Color |
| --- | --- | --- | --- | --- | --- | --- |
| Video |  | 2 |  | 4 |  | White |
| Ground |  | 4 |  | 1 |  | Green |
| Vert Sync |  | F |  | 9 |  | Black |
| Horz Sync |  | K |  | 8 |  | Red |

Depending on the video pigtail, the wire colors may change, but they will be labeled as to their connection.

VGA cable provided in kit could look like one of these.

Edge Card connector for video signals on the existing CBW processor board.

The wires below are marked with signal names.  Match these to the signal names on the new monitor cable and connect wires using the terminals provided.